## Slide 1: SEQUENTIAL CIRCUIT
Flip-Flops

## Slide 2: D Flip-Flop – Modified ver. Of SR Flip-Flop. Only one Input.
CLK | S | R | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Invalid
T.T for S-R Flip-Flop
CLK | D | Qn+1
0 | X | Qn
1 | 0 | 0
1 | 1 | 1
T.T for D Flip-Flop

## Slide 3: J-K Flip-Flop – Refinement of SR F/F. Invalid state is defined.
CLK | S | R | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Invalid
T.T for S-R Flip-Flop
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Qn’
T.T for J-K Flip-Flop
S | R | Q | Q’
0 | 0 | Invalid | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory | 
T.T fo S-R Latch using NAND

## Slide 4: T Flip-Flop – Derived from JK Flip-Flop . One input
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Qn’
T.T for J-K Flip-Flop
CLK | T | Qn+1
0 | X | Qn
1 | 0 | Qn
1 | 1 | Qn’
T.T for T Flip-Flop

## Slide 5: Master Slave JK Flip-Flop

## Slide 6: Master Slave JK Flip-Flop
Combination of 2 JK flip-flops in series.
One acts as ‘master’ and the other as ‘slave’
It also includes an Inverter.
CLK | J | K | Qn+1
0 | X | X | Qn
1 | 0 | 0 | Qn
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | Qn’
T.T for J-K Flip-Flop

## Slide 7
When the clock is high, master is operational but slave is not operational(it will keep memory)
When the clock is low, master is not functional but slave is. The output at salve is fed back to master but the clock is low. So, In this case effect of feedback is eliminated(which eliminates racing)