## Slide 1: REAL TIME SYSTEM
Lecturer: Er. Saroj Ghimire
Qualification: Msc.CSIT, BE(COMPUTER)
Lincoln University College

## Slide 2: 3.A Reference Model of Real-time Systems
Processors and Resources
Temporal Parameters of Real-time Workload
  Fixed Jittered and Sporadic Release Times
  Execution Time
Periodical Task Model
  Periods, Execution Times and Phases of Periodic Tasks
  Aperiodic and Sporadic Jobs
Precedence Constraint and Data Dependency
  Precedence Graph and Task Graph
  Data Dependency

## Slide 3: Objectives
After studying this unit, you will be able to:
Describe Processors and Resources
Enumerate Temporal Parameters of Real-time Workload
Define Periodical Task Model
Explain Precedence Constraint and Data Dependency

## Slide 4: Introduction
A reference model of real-time systems is needed to focus on aspects of the system relevant to its real-time timing and resource properties.
A system may be characterized by 3 models:
  A workload model describing the applications (i.e. control laws and their time complexity) supported by the system;
  a resource model describing the system resources (e.g., compute cycles or time on the processor hardware to be used) available to the applications.
  The scheduling and resource management algorithms define how the application uses the resources (i.e. how the workload is scheduled on the system).

## Slide 5: 1.Processors and Resources
All the resources can be divided into two parts:
Processors
  Two processors are of the same type of they are functionally identical and can be used interchangeably.
    Symmetric Multi-processors.
    Two transmission links connected with the same transmission rate between a pair of sender and receiver.
Resources
  By resources we specifically mean passive resources such as memory, mutexes, database locks.
  Resources always mean a re-usable resource. A resource is plentiful if no job is ever prevented from execution by the lack of this resource, i.e. a resource that can be shared by infinite number of jobs for example a file readable by all

## Slide 6: 2.Temporal Parameters of Real-time Workload
The number of tasks is one parameter. In most embedded systems, the number of tasks is fixed in a particular operation mode. In some systems, however, the number of tasks may change as tasks are added or deleted while the system executes. In an air traffic controller, each surveillance task monitors a single aircraft. The number of tasks may change (added or deleted) when aircrafts enter or leave the coverage area.
Each job is characterized by temporal parameters, functional parameters, resource parameters, and interconnecting parameters.
  Temporal parameters tell us its timing constraints.
  Functional parameters specify the intrinsic properties of job.
  Resource parameters give us its resource requirements
  Interconnection parameters describe how it depends on other jobs and others depend on it.

## Slide 7: 2.Temporal Parameters of Real-time Workload(contd)
Fixed Jittered and Sporadic Release Times
  In many systems, we do not know the actual release time ri of each job Ji, we are given a range [ri- ,ri+]. It can be as earliest as ri- or as late as ri+. This range is called release time jitter. Almost every real-time system is required to respond to external events which occur at random instants of time. On such events the system executes a set of jobs in response. The release time of these jobs is not known until the event triggering them occurs
  These jobs are called sporadic or aperiodic jobs as these are released at random time. The pilot may disengage the autopilot system at any time. When this occurs; the autopilot system changes from cruise mode to standby mode. The jobs which executed for this mode change are sporadic
Execution Time
  Another temporal parameter of a job, Ji, is its execution time, ei.
  It the time required to complete the execution of Ji when it executes alone and has all the resources it requires.
  The actual amount of time to complete its execution may vary for reasons like execution depending on the input data. The actual amount of time to transmit each frame of MPEG compressed video is different from frame to frame, because of the number of bits used to encode different frames.
  What can in fact be determined a priori are the maximum and minimum amounts of time required to complete each job (analysis and measurement and testing) We know that the execution time ei of the job Ji is in the range [ei+, ei+].

## Slide 8: 3.Periodical Task Model
Periods, Execution Times and Phases of Periodic Tasks
  Each computation or data transmission that is executed repeatedly at regular or semi-regular time intervals in order to provide a function of the system is modelled as a period task. Simply a periodic task occurs at regular intervals.
  Each task Ti is characterized by the following parameters.
    The release time (r): the time when the task first released.
    The period (T): the constant interval between jobs.
    The relative deadline (D): the maximum acceptable delay for task processing.
    The computation time (C): the worst case execution time (WCET) of any job.
    The tasks in the system can be denoted by T1 , T2 ,…,Tn .
    Individual jobs in a task Ti can be denoted as Ti,1, Ti,2….Ti,n
    The release time ri,1 of the first job Ji,1 in each task Ti is called the phase of Ti. Different tasks may have the same phase
Job is released at time 3. Its (absolute) deadline is at time 10. Its relative deadline is 7. Its response Notes time is 6. A time interval of length H is called a hyper period of the periodic tasks. It is the least common multiple of pi for i=1, 2, …n. The length of a hyper period of three periodic tasks with periods 3, 4, 10 is 60
The maximum number N of jobs in each hyper period is equal to summation value of H/pi.
The total number of job in the hyper period is 41. The ratio ui = ei/pi is the utilization of the task Ti.
Ui is equal to the fraction of time a truly periodic task with period pi and execution time ei keeps a processor busy.
The total utilization U of all the tasks in the system is the sum of the utilizations of the individual tasks in it. If the execution times of the three periodic tasks are 1, 1, 3 and periods are 3,4,10 then their utilizations are 0.33, 0.25 and 0.3. Total utilization is 0.88 (These tasks keep processor busy 88% of time).

## Slide 9: 3.Periodical Task Model(contd)
Aperiodic and Sporadic Jobs
  A task is aperiodic if the jobs in it have either soft deadlines or no deadlines. The task to adjust radar’s sensitivity is an example
  We want the system to be responsive, that is, to complete each adjustment as soon as possible. But a late response is annoying but tolerable. We therefore want to optimize the responsiveness of the system for the aperiodic jobs, but never at the expense of hard real-time tasks has whose deadlines must be met at all timed.
  Tasks containing jobs that are released at random time instants and have hard deadlines are sporadic tasks.
  In contrast, an autopilot system is required to response to a pilot’s command to disengage the autopilot and take over the control manually within a specific time. The jobs that execute in response to these events have

## Slide 10: 4.Precedence Constraint and Data Dependency
Data and control dependencies among jobs may constrain the order in which they can execute.
The jobs are said to have precedence constraints if they are constrained to execute in some order.
If the jobs can execute in any order, they are said to be independent.
Consider queries to an information server. Suppose that before each query is processed and the requested information retrieved, its authorization to access the requested information is first checked. The retrieval job cannot begin execution until the authentication job completes.
Similarly in a communication system, the jobs that generate acknowledgements of a message and transmit the acknowledgement message cannot begin until the job that receives and processes the message completes

## Slide 11: 4.Precedence Constraint and Data Dependency(contd)
Precedence Graph and Task Graph
  We use a partial-order relation <, called a precedence relation, over the set of jobs to specify the precedence constraints among jobs.
  A job Ji is a predecessor of another job Jk if Jk cannot begin execution until the execution of Ji completes.
  In short we can write Ji < Jk. Ji is the immediate predecessor of Jk if Ji < Jk and there is no other job Jj such that Ji<Jj<Jk.
  Two jobs are independent when neither Ji<Ji
  A job with predecessors is ready for execution when the time is at or after its release time and all of its predecessors is completed. A task graph, which gives us a general way to describe the application system, is an extended precedence Graph. The vertices in a task graph represent jobs.
  The task represented in first row has phase 0, period 2 and relative deadline 7 and all jobs are independent. The jobs released in later periods are ready for execution as soon as they are released even though some job released earlier is not yet complete. The second row represents a periodic task has phase 2, period 3 and relative deadline 3 and jobs are interdependent. The first job is predecessor of 2nd and 2nd is predecessor of 3rd job. The last two tasks are not periodic

## Slide 12: 4.Precedence Constraint and Data Dependency(contd)
Data Dependency
  Data dependency cannot be captured by a precedence graph. In many real-time systems, jobs communicate via shared data. Each producer can place the data generated by it in a shared address space to be used by the consumer at any time so precedence graphs shows them as independent.
  What if consumer and producer need to be synchronized? In an avionics system, the navigation job updates the location of the air plane periodically. Whenever the flight management job needs navigation data, it read the most current data produced by the navigation data from the shared space. Data dependencies among jobs are represented explicitly by data dependency edges among jobs

## Slide 13: Self Assessment
Fill in the blanks:
  A ……………… model of real-time systems is needed to focus on aspects of the system relevant to its real-time timing and resource properties.
  A system may be characterized by ……………… models.
  A ……………… model describes the applications.
  A ……………… model describes the system resources.
  The scheduling and ……………… algorithms define how the application uses the resources.
  Resources always means a ……………… resource.
  State whether the following statements are True or False:
    Each computation or data transmission that is executed repeatedly at regular or semi regular time intervals in order to provide a function of the system is modeled as a period task.
    A periodic task occurs at irregular intervals.
    A task is said to be periodic if the jobs in it have either soft deadlines or no deadlines.
    The jobs are said to have precedence constraints if they are constrained to execute in some order.
    If the jobs can execute in any order, they are said to be dependent.
    Data dependency cannot be captured by a precedence graph.

## Slide 14: Self Assessment Answer
1. Reference 2. Three 3. Workload 4. Resource 5. Resource management 6. Re-usable 7. True 8. False 9. False 10. True 11. False 12. True

## Slide 15: Further Readings
Alan Burns and Andy Welling's (2001). Real-Time Systems and Programming Languages, Addison Wesley. C. M. Krishna and K. G. Shin (1997).
Real-Time Systems. McGraw-Hill International Editions. O’Reilly Editor (1995).
Programming for the real world. Ben-Ari, M. (1990). Principles of Concurrent and Distributed Programming, Prentice Hall.